Settings to be checked	Target	Actual
Planning the installation	Is there a guide for installing new domain controllers? / The guide should include the following points: / Selection of the operating system / Size of the RAM / Size of the hard disk (partitions) / Number of CPUs / Connection to the monitoring
partitioning of the systems	The directories /var /usr /home /boot should be installed on their own partitions. The partitions /usr and /boot should be mounted read-only. These partitions should only be writable during the system update.
Install services and packages after the basic installation.	Which additional packages and services were installed on the domain controllers? Samba does not need to be considered here.
Who has access to the log files? Is there a central log host to store all log files centrally	Log files from all domain controllers should be stored on a central log host so that the log can still be accessed in the event of a security incident. This way, an attacker does not have the option of manipulating log files.
Updates	There should be instructions on how and when to update the server. It should also be documented who is responsible for the updates. The update history should be logged.
Network configuration	If IPv6 is not needed, it should be disabled system-wide. Only the required network interfaces should be configured.
Local packet filters	Since a domain controller requires a large number of ports, a local packet filter on domain controllers is difficult to implement.
Connection to the monitoring	All domain controllers should be monitored. Important points: / - CPU utilization / - memory utilization / - utilization of the partitions
Security check of the operating system	The system should be regularly checked for unauthorized logins. The installed packages should be regularly checked against a CVE database such as: / https://www.cvedetails.com/ should be carried out regularly. Especially if the system update is carried out from local update servers.
Use of HIDS (Host based Intrusion Detection	In order to detect attacks on a local system as quickly as possible, systems such as: / - tripwire / - chrootkit / should be used.
Operating manual	There should be an operating manual in which all changes and the installation of all packages are documented. The manual should also define the lifespan of the servers so that a new installation or a system update can take place at an early stage.
Access control	All access should be documented in the log, especially access by external employees. Access as “root” should be specially monitored and restricted.